## Slide 1
iOS Dev Camp #3 Week 5 View Controller Lifecycle
Edward Chiang
2014.11.03 - 2014.11.07

## Slide 2: Today
View Controller Lifecycle

## Slide 3: View Controller Lifecycle
5

## Slide 4: View Controller Lifecycle
View Controller have a “Lifecycle”
  A sequence of messages is sent to them as they progress through it.
Why does this matter?
  You very commonly override these methods to do certain work.
The start of the lifecycle
  Creation.
  MVCs are most often instantiated out of a storyboard.
  There are ways to do it in code as well which we may cover later.

## Slide 5: View Controller Lifecycle
What then?
  Outlet setting.
  Appearing and disappearing.
  Geometry changes.
  Low-memory Situations.
  At each stage, iOS invokes method(s) on the controller.

## Slide 6: ViewDidLoad
After instantiation and outlet-setting, viewDidLoad is called.
  This is an exceptionally good place to put a lot of setup code.
    - (void)viewDidLoad {
      [super viewDidLoad];
      // do some setup of MVC
    }
  Be careful because the geometry of your views(bounds) not set yet!
  At this point, you can’t be sure you’re on an iPhone 5 sized screen or an iPad or ????.
  If you need to initialize something based on the geometry of the view, use viewWillAppear

## Slide 7: ViewWillAppear
Just before the view appears on screen, you get notified.
Your view will only get “loaded” once, but it might appear and disappear a lot.
Don’t put something in this method that really wants to be in viewDidLoad. Otherwise, you might be doing something over and over unnecessarily.
Do here if things you display are changing while your MVC is off-screen.
This method is for
  Geometry-related initialization.
  Lazy execution.
  Late updating.

## Slide 8: ViewWillDisappear
You get notified when you will disappear off screen too.
There are “did” version of both of the appearance methods.
  - (void)viewDidAppear:(BOOL)animated;
  - (void)viewDidDisappear:(BOOL)animated;

## Slide 9: Geometry changed?
Most of the time this will be automatically handled with Autolayout.
Call any time a view’s frame changed and its subviews were thus re-layed out.

## Slide 10: Autorotation
When the device is rotated, the top level view controller will have its bounds reoriented
  The view controller returns YES from shouldAutoroated.
  The view controller returns the new orientation in supportedInterfaceOrientations.
  The application allows rotation to that orientation (defined in Info.plist file).
(void)willRotateToInterfaceOrientation:(UIInterfaceOrientation)anOrientation duration:(NSTimeInterval)seconds;
(void)willAnimateRotationToInterfaceOrientation:(UIInterfaceOriention)orient duration:(NSTimeInterval)seconds;
(void)didRotateFromInterfaceOrientation:(UIInterfaceOrientation)anOrientation;
It’s pretty rare to implement these. Autolayout and viewWillLayoutSubvies usually suffice.

## Slide 11: awakeFromNib
This method is sent to all objects that come out of a storyboard (including your Controller). Happens before outlets are set! (i.e. before the MVC is “loaded”)
Put code somewhere else if at all possible (e.g. viewDidLoad or viewWillAppear:).
Anything that would go in your Controller’s init method would have to go in awakeFromNib too (because init methods are not called on objects that come out of a storyboard).

## Slide 12: Simply through
ViewDidLoad - Called when you create the class and load from xib. Great for initial setup and one-time-only work.
ViewWillAppear - Called right before your view appears, good for hiding/showing fields or any operations that you want to happen every time before the view is visible. Because you might be going back and forth between views, this will be called every time your view is about to appear on the screen.
ViewDidAppear - Called after the view appears - great place to start an animations or the loading of external data from an API.
ViewWill/DidDisappear - Same idea as WillAppear.
ViewDidUnload/ViewDidDispose - In Objective C, this is where you do your clean-up and release of stuff, but this is handled automatically so not much you really need to do here.

## Slide 13: Summary
Instantiated (from storyboard - many ways for this to happen which we’ll cover later) awakeFromNib, viewDidLoad
(when geometry changes) viewWillLayoutSubviews: and viewDidLayoutSubviews:
(next group can happen repeatedly as your MVC appears and disappears from the screen …) viewWillAppear: and viewDidAppear:

## Slide 14
~ END ~
http://www.alphacamp.tw